## ROS Camera Driver

Installation

1. Get the file cam611_driver and unpack it in for example ~/projects/cam611_driver folder.
2. Compile it:
> cd ~/projects/cam611_driver
> catkin_make
> source ~/projects/cam611_driver/develop/setup.bash

Running

espros_cam611 package has two nodes: cam611_range and cam611_frame.

Depending on the connected camera can launch selected node:
roslaunch espros_cam611 range.launch
roslaunch espros_cam611 frame.launch

ROS API

cam611_range

Published Topics

range/distance_range (sensor_msgs/Range)
The confidence range pixel represents distance value in mm.
range/amplitude_range (sensor_msgs/Range)
The confidence range pixel represents the amplitude value in LSB.

Parameters

Static Parameters

port_name(string, default: "/dev/ttyUSB0")
The device path to open serial port.

Dynamically Reconfigurable Parameters

See the dynamic_reconfigure package for details on dynamically reconfigurable parameters.

~range_data_type (int, default: 0)
Data acquisition type: distance – 0, distance_amplitude – 1.
~frame_rate (double, default: 30.0)
Acquisition rate at which the data are captured [Hz].
~start_stream (bool, default: false)
Enable data streaming.
~trigger_single_shot (bool, default: false)
Trigger single measurement by changing state from false to true.
~auto_integration_time(bool, default: true)
Enable automatic integration time mode
~integration_time_tof(int, default: 200)
Sets the integration time in microseconds for distance measurements. Range: 1 … 1600 µs.
~temporal_filter_factor (double, default: 0.01)
Sets the factor of temporal Kalman filter. Range 0.0 ... 1.0.
~temporal_filter_threshold (int, default: 300)
Sets the threshold for temporal Kalman filter. Range 0 … 20000 mm (uses to filter out temporal noise in an image).
~modulation_frequency(int, default: 1)
Sets the modulation frequency. 0 – 10 MHz, 1 – 20 MHz.

cam611_frame

Published Topics

image/distance_image (sensor_msgs/Image)
The confidence 8x8 image (each pixel depending on selected image type represents the distance value).
image/amplitude_image (sensor_msgs/Image)
The confidence 8x8 image (each pixel represents the amplitude value).

Static Parameters

port_name(string, default: "/dev/ttyUSB0")
The device path to open serial port.

Dynamically Reconfigurable Parameters

See the dynamic_reconfigure package for details on dynamically reconfigurable parameters.

~image_type (int, default: 0)
Image acquisition type: distance – 0, distance_amplitude – 1.
~frame_rate (double, default: 30.0)
Acquisition rate at which the frames are captured [Hz].
~start_stream (bool, default: false)
Enable image streaming.
~trigger_single_shot (bool, default: false)
Trigger single measurement by changing state from false to true.
~integration_time_tof(int, default: 200)
Sets the integration time in microseconds for distance measurements. Range: 1 … 1600 µs.
~temporal_filter_factor (double, default: 0.01)
Sets the factor of temporal Kalman filter. Range 0.0 ... 1.0.
~temporal_filter_threshold (int, default: 300)
Sets the threshold for temporal Kalman filter. Range 0 … 20000 mm (uses to filter out temporal noise in an image).

Notes:
1. TOF> Frame uses modulation frequency 20MHz.
2. cam611_driver is tested with ROS Noetic, Melodic and Kinetic versions.
3. If you want to connect more tof range or frame devices, you have to change static parameter port_name.